CONTROL

CAR SECURITY SYSTEM

# OWNER'S  MANUAL

CONTENTS:

## OPERATING INSTRUCTIONS

DESCRIPTION OF FUNCTIONS AND FEATURES

WIRE CONNECTION GUIDE

INSTALLATION GUIDE

KD300E (upgrading alarm with original remote)

OPERATING  INSTRUCTIONS

FUNCTION SETTING

| FUNCTION | JP Position | METHOD |
| --- | --- | --- |
| Auto Re-Arming Operation | JP1 | Open circuit (production inside setting) |
| NOTE: ICON OF INDICATING SHORT CIRCUIT & OPEN CIRCUIT. ( ：<< SHORT ) (：<< OPEN ) 2. DO ALL SETTING IN NO POWER SUPPLIED CONDITION. |

# DESCRIPTION OF FUNCTIONS & FEATURES

###### ARM ING

- Press LOCK button of the original remote, siren will chirp once and lights flash once.

- The power window will close up automatically for 25 seconds.

- The engine is locked, the L.E.D flashe, the alarm is armed.

- DISARM ING

- Press UNLOCK buttoN of the original remote, siren will chirp twice and lights flash twice

- Alarm is disarmed, and the LED stops flashing and the engine can be started.

- CAR SEARCHING/PANIC

First time press LOCK,the system in arming mode, press LOCK again to be activated.

- ORIGINAL CAR KEY CONTROL

In arming mode, if use the original car key to open the door, the system will be in trigger alert, after using the original car remote to disarm the alarm, the system can be unlock.

# SPECIAL  FEATURES

1.AUTO RE-ARMING OPERATION(option)

If nobody enters the car in 20+/-5 seconds after the system is disarmed by pressing UNLOCK button, the door of the car will automatically be locked again and the system will come back to be on "ALERT" mode.

2. AUTO CENTRAL LOCK

When driving, press LOCK or UNLOCK to lock or unlock the doors, but the alarm system will not be set work. Turn on the ignition after closing the car doors in a proper way, step on the foot brake and the car doors will be locked automatically. Please note: The doors will not be locked automatically if the ignition key is not turned to the "ACC. ON" position or if the doors are not closed properly.

The car doors will automatically unlocked when the key is taken out of the ignition switch.

3. WARNINGS OF ABNORMAL SITUATION

If the alarm system is triggered in arming mode, then:

- The siren will sound 15 seconds in arming mode when the car window is knocked or when the car body is bumped.

- The siren will keep on sounding for 25 seconds when the car door is opened or when the engine is ignited illegally.

4. TRIGGER MEMORY

If the system is triggered, the LED will quick flash, when press UNLOCK button,the siren will short chirp for 4 times. When open the door, the siren will sound 1 time to give warning to the car owner to check the car inside and outside to make sure about the safety of the car.

5. MEMORY ALARM MODES

If the car power is cut off whether the system is armed or disarmed, the system will still keep in original condition.

If alarm cycles have triggered ,the siren will be given different sound to show which trigger cause the alarm:

- 4 times sound followed by a pause for shock sensor and ultrasonic sensor

- 5 times sound followed by a pause for door opening

- 6 times sound followed by a pause for attempted engine starting

The signal will continue to be given until the engine is switched on or the system is armed again.

6.POWER WINDOW FUNCTION(OPTION)

Press LOCK button one time, the siren will chirp once and light flash once, and the power window will close up automatically. It lasts at 25 seconds.

7. EMERGENCY OVERRIDE (RESET) FUNCTION

If the original remote is lost or damaged, the car owner can use his key to get into the car. Then press reset switch for 5 seconds in ON position to disarm the system.

8. AUTO-DELAY ENTERING ARMING

The system will delay to enter arming until the doors are closed exactly or the interior light to be OFF.

# WIRE CONNECTION DIAGRAM

See attachment to reference.

# CENTRAL DOOR LOCK INSTALLATION DIAGRAM

See attachment to reference.

# SYSTEM INSTALLATION GUIDE

Main Unit Installation

The main unit is suggested to placed under the panel. After fixing the main unit in a suitable place, start connecting the wires in accordance to the WIRE CONNECTING DIAGRAM before putting back all the parts, simply test the system function first.

Shock Sensor Installation

Install the sensor after fixing the main unit .It is recommended to place the shock sensor near the car doors, or beside the panel so as to easily detect any intrusion actions. To adjust the sensitivity of the shock sensor, simply use a screw to turn the button in the shock sensor, turning right to adjust with a higher sensitivity or vice verse. Then test the sensitivity by triggering the shock sensor. If it triggered, the L.E.D will light up. Please do not directly hit the shock sensor.

# SPECIFICATIONS OF ELECTRONIC

MAIN UNIT

Output current:          signal light 5A*2, siren 10A, central lock:10A

Coding:                learning code

Voltage:                12+2V

Static Current:           <15mA( except indicator, sensor)

Indicator Current :        20mA intermittently

Shock Sensor Current:     <1mA

# TROUBLE SHOOTING

The remote control does not work.

*Check the battery level. It is suggest to replacing a new battery each year.

*Check if the remote control is moisten or crash.

The remote control does not make the main unit work.

*Check the battery level in the remote control.

*Check if the remote control is moisten or crash.

*Check if the frequency of the remote control is changed.

*If possible, use another control for comparison. If both of them do not work, then check the main unit and the wire connection.( Do not open the main unit for checking)

The central lock does not work.

*Check if the actuators are working.

*Check wire connection

*Check if the fuse of the main unit is damaged.

The siren does not sound when the system is triggered.

*Check if the sirens are available.

*Check the wire connection between the siren and main unit.

The siren keeps chirping while the main unit installs.

*Check if the socket is insert converse or check the wires connection or the CPU safety fuse.

*If back up battery is used, check if the switch is positioned at ON status.

The alarm sounds 10 seconds after the vehicle is armed, same problem keeps happening again.

*Check if the shock sensor is too sensitive.

*Check if the door pin switches are damaged.

*Check wire connection.

The alarm is easily triggered when a heavy vehicle is passing through.

*Check if the shock sensor is too sensitive.

# Text boxes

### OWNER’S WARRANTY RECORD

(To be completed by selling dealer)

WIRE CONNECTION DIAGRAM

Customer's Name：

Address：

Purchase Date：

Dealer Name：

Dealer Address：

Alarm system code number：

Alarm system model：

Date Installed：

Note: