CONTROL

CAR SECURITY SYSTEM

# OWNER'S  MANUAL

CONTENTS:

## OPERATING INSTRUCTIONS

DESCRIPTION OF FUNCTIONS AND FEATURES

WIRE CONNECTION GUIDE

INSTALLATION GUIDE

KD3006F

OPERATING  INSTRUCTIONS

3 BUTTON REMOTE CONTROL

| FUNCTION | ARM | DISARM | MUTE ALARM | CAR SEARCH | TRUNK RELEASE |
| --- | --- | --- | --- | --- | --- |
| PRESS |  |  | + |  | Press 2S |

4 BUTTON REMOTE CONTROL

| FUNCTION | ARM | DISARM | MUTE ALARM | CAR SEARCH | TRUNK RELEASE |
| --- | --- | --- | --- | --- | --- |
| PRESS |  |  |  |  | Press 2S |

5 BUTTON REMOTE CONTROL

| FUNCTION | ARM | DISARM | MUTE ALARM | CAR SEARCH | TRUNK RELEASE |
| --- | --- | --- | --- | --- | --- |
| PRESS |  |  |  |  | Press 2S |

FUNCTION SETTING

| FUNCTION | JP Position | METHOD |
| --- | --- | --- |
| OPEN DOOR, LIGHT FLASH | JP1 | Short circuit: yes (Factory Default) Open circuit: no |
| NOTE: THE SYSTEM IS SET IN JP1 SHORT CIRCUIT AS DEFAULT. DO ALL SETTING IN NO POWER SUPPLIED CONDITION, OTHERWISE WORLESS. |

# DESCRIPTION OF FUNCTIONS & FEATURES

###### ARM THE ALARM

- Siren will chirp once and lights flash once.

- If equipped with central door lock, doors lock automatically.

- After 4 seconds, the engine is cut-off, the L.E.D blinks, indicating the system enter into ALERT mode.

- If the door is not closed properly, when you arm the alarm, the siren will chirp 5 times to remind the car owner.

DISARM THE ALARM

- Siren will chirp 2 times and lights flash 2 times.

- Driver’s door unlock automatically. Press again to unlock other doors.

- Alarm is disarmed and returns to its normal status.

- If nobody enters the car after 25 seconds, the system will come back to alert mode again.

Please also refer to “AUTO REARMING” feature.

SILENT ALARM MODE

- Lights flash once, but siren will not chirp.

- If the alarm shock is triggered, lights will flash, but siren will not sound.

- If illegally enter, the siren will chirp immediately, and will stop in 25±5 seconds, return to arming mode.

PANIC, CAR SEARCH

- Press  again in arming mode, the siren sound with lights flash 15 seconds. Press again to stop.(for 3 button only)

- Press  in silent arming mode, the siren will not sound and lights will flash for 15 seconds. Press again to stop.

- After the 15 seconds alarm cycle, the system will return to its previous status (armed or disarmed or silent alarm mode).

STOP SIREN TEMPORARILY

If alarm system is triggered off, the siren will blare. By pressing or  to stop the siren temporarily but the alarm system is still on arming mode.

F)  ANTI-HIJACKING

When driving, Press the button or press + at the same time for 2 seconds, the parking lights flash quickly and the siren sound intermittently

after 30 seconds, the engine will be cut off and siren stop sounding and parking lights stop flashing. Press to stop the function. If you don’t cancel anti-hijacking, the system will keep alarming every other 10 seconds.

# SPECIAL  FEATURES

1.MISS-TOUCH

Once the vehicle started accidentally touching buttons that normally arm the alarm, will not arm the alarm, but will lock doors. Press disarm button to unlock the doors.

2.AUTO RE-ARM

If nobody enters the car in 25+/-5 seconds after the system is disarmed by pressing button , the door of the car will automatically be locked again and the system will come back to be on "ALERT" mode.

3. AUTO CENTRAL LOCK

When driving, press  or to lock or unlock the doors, but the alarm system will not be set work. Turn on the ignition after closing the car doors in a proper way, after 5 seconds, step on the foot brake and the car doors will be locked automatically. Please note: The doors will not be locked automatically if the ignition key is not turned to the "ACC. ON" position or if the doors are not closed properly.

The car doors will automatically unlocked when the key is taken out of the ignition switch.

4. OPEN DOOR, LIGHT FLASH(WARNINGS OF IMPROPER CLOSED OF DOORS(JP1 optional))

If the doors are not properly closed, the lamps will keep flashing for 15+/-5 seconds in order to give warnings to the cars behind.

5. WARNINGS OF ABNORMAL SITUATION

If the alarm system is triggered in arming mode, then:

- The siren will sound on in arming mode (without sounding in silent mode) when the car window is knocked or when the car is bumped.

- The siren will keep sounding for 25+/-5 seconds when the car door is opened or when the engine is ignited illegally.

6. TWO STAGE SIREN VERIFICATION

When the shock sensor is triggered, the siren will chirp 3 times, the parking light will flash 3 times; If the shock sensor is triggered again in 15 seconds, the siren will chirp intermittently for 30 seconds(in mute alarm mode, the siren will not chirp) and the parking light will flash for 30 seconds, Led will flash 3 times every other 2 seconds.

7. MEMORY ALARM MODES

If the car power is cut off whether the system is armed or disarmed, the system will still keep in original condition.

8. TRUNK RELEASE FUNCTION

In disarm mode, press  button for 2 seconds, the trunk will be released automatically.(for 3 and 5 button)

In disarm mode, press  button for 2 seconds, the trunk will be released automatically.(for 4 button only)

9. RESET FUNCTION

When the remote control is damaged or the battery out of power, open the door, press always on the foot brake, turn the ignition key from OFF-ON for 5 times and keep the ON position, the alarms system will return to the Disarm situation.

10. SILENT MODE (for 3 key remotes)

Under disarming mode, press  +, the siren will not chirp.

16.CODE LEARNING MODE

In this mode, the safety and reliability of the system are greatly increased for coding times over 1 million.

New code learning procedure:

- During disarming status, stay inside the car , close the door properly, then step always on the foot brake, open the door (now the lamps flashing).

- Turn the ignition key from OFF-ON--OFF-ON-OFF-ON position3 times, and keep ON position (now the lamps keep lighting). Press any key of the remote control, the sirens will chirp 3 times after 3 seconds, indicating that a new code is stored. Once remote is learnt successfully, Press another remote, the sirens will chirp 3 times after 3 seconds. Store the code of the third and the fourth remote by pressing any key of the remote.

NOTE: All operating should be finished within 5 seconds, otherwise the system will cancel this learning.

This system can be learnt up to 4 remote.

(the system can learnt 4 remotes in one time, when the new remote is learnt, the old remote is invalid)

# SYSTEM INSTALLATION GUIDE

Main Unit Installation

The main unit is suggested to placed under the panel. After fixing the main unit in a suitable place,  start connecting the wires in accordance to the WIRE CONNECTING DIAGRAM before putting back all the parts, simply test the system function first.

Shock Sensor Installation

Install the sensor after fixing the main unit .It is recommended to place the shock sensor near the car doors, or beside the panel so as to easily detect any intrusion actions. To adjust the sensitivity of the shock sensor, simply use a screw to turn the button in the shock sensor, turning right to adjust with a higher sensitivity or vice verse. Then test the sensitivity by triggering the shock sensor. If it triggered, the L.E.D will light up. Please do not directly hit the shock sensor.

# SPECIFICATIONS OF ELECTRONIC

MAIN UNIT

Output current:          signal light:5A*2, siren 10A, central lock 10A

Coding:                learning code

Voltage:                12+2V

Static Current:           <15mA( except indicator, sensor)

Indicator Current :        20mA intermittently

Shock Sensor Current:     <1mA

Frequency:              315MHz

REMOTE CONTROL

Voltage:                12V

Current:                0mA

Battery:                27A/12V

Frequency:             315MHz

Coding:               learning code

# TROUBLE SHOOTING

The remote control does not work.

*Check the battery level. It is suggest to replacing a new battery each year.

*Check if the remote control is moisten or crash.

The remote control does not make the main unit work.

*Check the battery level in the remote control.

*Check if the remote control is moisten or crash.

*Check if the frequency of the remote control is changed.

*If possible, use another control for comparison. If both of them do not work, then check the main unit and the wire connection.( Do not open the main unit for checking)

The central lock does not work.

*Check if the actuators are working.

*Check wire connection

*Check if the fuse of the main unit is damaged.

The siren does not sound when the system is triggered.

*Check if the sirens are available.

*Check the wire connection between the siren and main unit.

The siren keeps chirping while the main unit installs.

*Check if the socket is insert converse or check the wires connection or the CPU safety fuse.

*If back up battery is used, check if the switch is positioned at ON status.

The alarm sounds 10 seconds after the vehicle is armed, same problem keeps happening again.

*Check if the shock sensor is too sensitive.

*Check if the door pin switches are damaged.

*Check wire connection.

The alarm is easily triggered when a heavy vehicle is passing through.

*Check if the shock sensor is too sensitive.

------------------------------------------------------------------------------------------------------------------------------

### OWNER’S WARRANTY RECORD

(To be completed by selling dealer)

Customer's Name：

Address：

Purchase Date：

Dealer Name：

Dealer Address：

Alarm system code number：

Alarm system model：

Date Installed：

Note:

WIRES CONNECTION DIAGRAM